## Slide 1: Lecture 8: ADB
Topics: Basic ADB Commands

## Slide 2: What is ADB?
Android Debug Bridge (ADB) is a command line utility to communicate with your Android device.
Uses:
  Listing connected devices.
  Installing and debugging apps.
  Copy files to and from the phone.
  Take screenshots, record screens, etc.
<android_sdk_path>/platform-tools/adb.exe
Notes: Power manage: wake lock, reboot.

## Slide 3: ADB Client-Server Architecture
Three entities are involved: a client, a server, a daemon (adbd).
Server
Daemon
Port: 5037
Port: 555X
Client
Background
process
Background
process
Invoked From
Terminal
Notes: Power manage: wake lock, reboot.

## Slide 4: Connecting over USB
Remember the first thing we did with the phone?
Settings>About Phone> Build number
Settings>Developer options> USB Debugging
Why?
Notes: Power manage: wake lock, reboot.

## Slide 5: Testing the ADB
Use a shell to invoke your first command:
USB
adb devices -l
List of devices attached
071b799a344bdc6b device product:hammerhead model:Nexus_5 device:hammerhead
Notes: Power manage: wake lock, reboot.

## Slide 6: When things go wrong …
Use a shell to kill and start the server:
USB
adb kill-server
adb start-server
* daemon not running. starting it now at tcp:5037 *
* daemon started successfully *

## Slide 7: ADB over WiFi
Set TCP port (over USB) and connect (over WiFi)
adb tcpip 5555
(USB must be connected)
adb connect [Phone’s IP Addr]
(USB must be disconnected)
To get your phone’s IP address: adb shell ifconfig

## Slide 8: ADB Commands
Now, you can communicate with the phone.
adb shell screencap /sdcard/s.png
adb pull /sdcard/s.png <local>
or

## Slide 9: Useful ADB Commands
Global Options:
adb –d <command>
adb –e <command>
adb –s <serial number> <command>
071b799a344bdc6b
071b799a344bdxyz

## Slide 10: Useful ADB Commands
General adb Commands:
adb devices -l
adb help
adb version
Network/File/Install adb Commands:
adb connect ip[:port]
adb disconnect ip[:port]
adb pull [-a] remote local
adb push local remote
adb install package
adb uninstall package

## Slide 11: Useful ADB Commands
backup/debug/scripting adb Commands:
adb backup [-f file] [-apk][-obb][-shared][-all][-system]
adb restore file
adb logcat [option]
adb root
adb unroot
adb usb
adb tcpip port_555X
adb start-server
adb kill-server
adb reconnect

## Slide 12: Issuing shell Commands
Activity Manager (am commands)
Generic format (two ways):
adb shell <command> (execute on device shell)
adb shell (get a device shell)
am start [option] intent (e.g., -a android.media.action.VIDEO_CAMERA)
am start
am startservice [option] intent
am broadcast [option] intent
am force-stop package
am kill [option] package
am kill-all
-n yourpackagename/.activityname

## Slide 13: Issuing shell Commands
Screen capture
Package Manager (pm commands)
pm list packages [options] filter
pm list permissions [options] filter
pm list features
pm list libraries
pm list users
pm install [options] path
pm uninstall [options] package
pm grant package permission
pm revoke package permission
screencap filename
screenrecord [option] filename

## Slide 14: Issuing shell Commands
Many more Unix commands!
ls
cd directory
chmod
df
mkdir
rm file
rmdir dir
ifconfig
iftop
netstat
ping host
echo text
date
time
reboot
ps
top

## Slide 15: Shell commands from Android APPs
Use ‘Runtime’ and ‘Process’ classes to issue shell commands from an Android app:
try { Process p = Runtime.getRuntime().exec("ps");
InputStreamReader isr = new InputStreamReader(p.getInputStream()); BufferedReader br = new BufferedReader(isr); String str ="";
while((str = br.readLine()) != null){ Log.v("Tag", str); } } catch (IOException e) { e.printStackTrace(); }

## Slide 16: References
https://developer.android.com/studio/command-line/adb.html
Notes: Power manage: wake lock, reboot.